## Slide 1: Extending Embedded System into PL
Zynq
Vivado 2014.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Identify the IP supplied as part of Vivado
  Describe how to add hardware to an existing Vivado project
  Explain how IP is added to extend processing system functionality

## Slide 3: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 4: The PS and the PL
The Zynq-7000 AP SoC architecture consists of two major sections
  PS: Processing system
    Dual ARM Cortex-A9 processor based
    Multiple peripherals
    Hard silicon core
  PL: Programmable logic
    Shares the same 7 series programmable logic as
      Artix™-based devices: Z-7010, Z-7015 and Z-7020 (high-range I/O banks only)
      Kintex™-based devices: Z-7030 and Z-7045, and Z-7100 (mix of high-range and high-performance I/O banks)
This sections focuses on the PL

## Slide 5: Communicating with PL
Processing system master
  Two ports from the processing system to programmable logic
  Connects the CPU block to common peripherals through the central interconnect
Processing system slave
  Two ports from programmable logic to the processing system
Slave PL peripherals address range
  4000_0000 and 7FFF_FFFF (connected to GP0) and
  8000_0000 and BFFF_FFFF (connected to GP1)
GP0 GP1

## Slide 6: IP Catalog
The IP Catalog contain a collection of IP that can be used to assemble the (embedded) system
Supported by IPI
Facilitates quick system construction
Each IP block has its own configuration parameters
Most of the IP is free, some require licenses
Stored as source code in the install directory
  Always synthesized with the latest tools
  Some proprietary source code is encrypted
Peripherals in the PS are always present and can be dynamically enabled or disabled through PS Configuration wizard

## Slide 7: IP Peripherals Included as Source (Free)
Bus and bridge controllers
  AXI to AXI connector
  Local Memory Bus (LMB)
  AXI Chip to Chip
  AHB-Lite to AXI
  AXI4-Lite to APB
  AXI4 to AHB-Lite
Debug cores
  Integrated Logic Analyzer
DMA and Timers
  Watchdog, fixed interval
Inter-processor communication
External peripheral controller Memory and memory controller
High-speed and low-speed communication peripherals
  AXI 10/100 Ethernet MAC controller
  Hard-core tri-mode Ethernet MAC
  AXI IIC
  AXI SPI
  AXI UART
Other cores
  System monitor
  Xilinx Analog-to-Digital Converter (XADC)
  Clock generator, System reset module
  interrupt controller
  Traffic Generator, Performance monitor

## Slide 8: Vivado IP Catalog
Integrated IP Support
  Instant access to IP customization
  Vivado IP GUI look and feel
  Support for Vivado synthesis and implementation
  Selectable IP output products
  Full Tcl support
Notes: Vivado has a unified IP catalog – all IP available in one place. The catalog can be extended through use of additional repositories. IP can be selected in the catalog and customization GUIs launched. IP is then added directly to a Vivado project, or in the case of IP Integrator, added to the diagram. The user can select simulation or implementation files. IP can be accessed and customized entirely from the Tcl console as well.

## Slide 9: IP Cores Included as Evaluation
AXI CAN controller
AXI USB2 device
Video IP
Telecoms/ Wireless IP
Xilinx developed, delivered, and supported
Evaluation IP installs with a 90-day evaluation license

## Slide 10: IP Cores
Right click to -
  Add/customize
  Determine compatibility
  Product Guide (datasheet) > Document Navigator
  Change Log
  Product Webpage
  Answer record
Export complete IP Catalog to excel

## Slide 11: IP Core Information
The size of each core is available in the data sheet
For example, the axi_timer_v2_00_a data sheet contains the following table:
Data sheet provided for each core (right-click on core in IP catalog to access)

## Slide 12: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 13: Peripheral Storage
IP Core directory (located in the project directory)
  {component}.xml
  MyProcessorIPLib directory (user defined)
    Repository Directory listed using Project  Project Options  Device and Repository Search tab
  %XILINX_INSTALL%\Vivado\2014.X\data\ip
User peripherals can be located in the project directory or a peripheral repository

## Slide 14: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 15: IP Core files
component.xml
  XML format
  Top level folder
  Provides ports description, parameters and options for IP
  Links to source files
xgui folder
  .tcl file for IPI GUI

## Slide 16: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 17: GP Ports
By default, GP Slave and Master ports are disabled
Enable GP Master and/or Slave ports depending on whether a slave or a master peripheral is going to be added in PL
axi_interconnect block is required to connect IP to a port with different protocols
  Automatically convert Protocols
  Can be automatically added when using Block Automation in IPI

## Slide 18: Configuring GP Ports
Click on the menu or green GP Blocks to configure

## Slide 19: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 20: Add IP in the PL
Configure GP ports from PS Customization GUI
PS-PL Configuration
    E.g. Enable M_AXI_GP0/1 or S_AXI_GP0/1
Ports will then be available on Zynq Block Diagram
Connect the added IP to the appropriate port
Assign address to the added IP, if unmapped
Configure the IP, if necessary
Make external connections, if needed
  Add external ports/interfaces if the added IP is interacting with external devices

## Slide 21: Connecting IP
Add IP from the IP Catalog
Click and drag to find connections
Valid connections Highlighted
Designer Assistance, Connection automation
    If Board Support available, IP can be connected to external pins
Or manually create and connect (external) ports

## Slide 22: Designer assistance; Block Automation, Connection Automation
Block, Connection
Can automatically connect IP blocks
Automatically insert required blocks
E.g. Add BRAM; Automation will insert and connect BRAM controller and Reset logic
If Board Support is available, IP can automatically be connected to top level ports

## Slide 23: Assign Addresses
Peripherals in the Zynq™ AP SoC PS have fixed addresses and do not appear in the address map when an IP is added to the system
For PS peripherals Click on the Auto Assign Addresses button
The address will be generated and show the generated addresses of the added IP
The fixed addresses of the configured peripherals of the PS

## Slide 24: Parameterize IP Instances
Double-click or right click the instance and select Customize Block to open the configurable parameters dialog box (refer to the datasheet if needed)
Default values are shown
  Customize the parameters that you want

## Slide 25: Extending the System
Import custom IP
IP Packager
  Packages into IP Integrator Format
Specify repository (local/global)
IP can then be used in IP Integrator
More on IP Packager later

## Slide 26: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 27: Bitstream Generation
After defining the system hardware, the next step is to create hardware netlists if the system hardware has logic in PL
A HDL wrapper for the block diagram must be generated
  Additional logic can be added to the HDL, or the Processor system can be used as a sub block in a HDL design
The design and block diagram must be open before synthesise and implementation can be carried out
If the system contains hardware in the PL, the bitstream must be generated
The PL (FPGA) must be programmed before application can be downloaded and executed

## Slide 28: Outline
IP Catalog
IP directory
IP device files
GP Interfaces
Adding IP to extend PS into PL
Bitstream generation
Summary

## Slide 29: Summary
PS functionality can be extended by instantiating peripherals in PL
Adding IP in PL involves
  Enabling interface(s) in PS
  Selecting IP from the IP Catalog and configuring IP for desired functionality
  Connecting the (PL) IP to the PS using IP Integrator
  Assigning address
  Connecting IP ports to ports of other peripherals and/or to external pins
HDL Wrapper is needed for IP Integrator Block
Bitstream must be generated when PL has any IP
The FPGA must be programmed with the generated hardware bitstream before an application can be run