## Slide 1: Lab2 Intro Adding IP in PL
Zynq
Vivado 2014.2 Version
Notes: Copyright 2013

## Slide 2: Introduction
This lab guides you through the process of extending the processing system you created in the previous lab by adding two GPIO IPs in PL

## Slide 3: ARM Cortex-A9 based Embedded System Design Lab2: Adding IPs in PL
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
Memory
GPIO
UART
RS232
DIP Switches
AXI4-Lite
GPIO
Push-Buttons
AXI4-Lite
M_AXI_GP0
PS
PL

## Slide 4: Procedure
Open the project in Vivado
Add and configure GPIO peripherals in the system in the IP Integrator
Add external ports
Generate the bitstream and export to SDK
Create a TestApp application in SDK
Verify the functionality in hardware

## Slide 5: Summary
The GP Master interface of the PS was enabled. GPIO peripherals were added from the IP catalog and connected to the Processing System through the 32b Master GP interface.
The peripherals were configured and external FPGA connections were established. Pin location constraints were made using IP Integrator Automation, and also manually, to connect the peripherals to push buttons and DIP switches.
A TestApp application project was created and the functionality was verified after downloading the bitstream and executing the program.