## Slide 1: Creating and Adding Custom IP
Zynq
Vivado 2014.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Describe the AXI4 transactions
  Summarize the AXI4 valid/ready acknowledgment model
  Discuss the AXI4 transactional modes of overlap and simultaneous operations
  Describe the operation of the AXI4 streaming protocol
  List the steps involved in creating and packaging IP

## Slide 3: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
Custom IP
Summary

## Slide 4: Basic AXI Transaction Channels
Read address channel
Read data channel
Write address channel
Write data channel
Write response channel
  Non-posted write model
    There will always be a "write response"

## Slide 5: All AXI Channels Use A Basic “VALID/READY” Handshake
SOURCE asserts and holds VALID when DATA is available
DESTINATION asserts READY if able to accept DATA
DATA transferred when VALID and READY = 1
SOURCE sends next DATA (if an actual data channel) or deasserts VALID
DESTINATION deasserts READY if no longer able to accept DATA

## Slide 6: AXI Interface: Handshaking
AXI uses a valid/ready handshake acknowledge
Each channel has its own valid/ready
  Address (read/write)
  Data (read/write)
  Response (write only)
Flexible signaling functionality
  Inserting wait states
  Always ready
  Same cycle acknowledge
Inserting Wait States
Always Ready
Same Cycle Acknowledge
Notes: It is up to the master to assert the valid signal and the slave to assert the ready signals for all channels except the read data channel where the slave asserts valid to indicate that it is returning data.
The agent that asserts ready determines the flexibility as seen in the three waveform options.

## Slide 7: AXI Interconnect
axi_interconnect component
  Highly configurable
    Pass Through
    Conversion Only
    N-to-1 Interconnect
    1-to-N Interconnect
    N-to-M Interconnect – full crossbar
    N-to-M Interconnect – shared bus structure
Decoupled master and slave interfaces
Notes: The AXI interconnect is added as any other component to the hardware in IP Integrator’s Block Diagram and then connected to the target processor and various IP bus cores provided by Xilinx.
The processor is always a master on the bus.
The actual implementation of the AXI interconnect is with slice combinatorial logic to implement the ORed structure of the decoupled address, data, and controls signals.
The context of “decoupled” refers to the fact that all the signals are unidirectional as inputs and outputs; that is, data in and data out, as opposed to a 3-state structure. The concept of a master is the bus agent that starts the transaction and owns the address out and control out signals.
  The Xilinx implementation of the AXI interface is documented in the Xilinx AXI Reference Guide (UG761).
  http://www.xilinx.com/support/documentation/ip_documentation/axi_interconnect/v1_05_a/ds768_axi_interconnect.pdf

## Slide 8: AXI4 Signals (AXI4, AXI4-Lite)

## Slide 9: AXI4 signals
ID – Identification signal
LEN – Burst length; 256 INCR, 16 Wrap
Size – Transfer width 8-256 bytes
Burst – INCR, WRAP, FIXED
Lock – Exclusive, atomic access
CACHE –Transaction caching
PROT – Access Protection
QOS – QOS signal
Region – allows multiple logical interfaces on slave
User – User signal
STRB – strobe
LAST – Indicate last transaction in burst
See AMBA® AXI™ and ACE™ Protocol Specification
Notes: ID – transaction ordering. Read transactions on the same master with same ID must complete in order they were presented. Same for write, but no requirement to preserve order of read and writes together. Facilitates overlapped transactions
Not usually implemented in Xilinx IP:
LOCK – Support atomic accesses; Normal, exclusive (semaphore without requiring LOCK), lock
CACHE signal can be used to determine which component provides the write response. If a write transaction is indicated as bufferable then it is acceptable for a bridge or system level cache to provide the write response. If, however, the transaction is indicated as being non-bufferable then the write response must be provided from the final destination of the transaction.
PROT Protection against illegal transactions. PROT gives three levels of access protection:
Normal or privileged
This is used by some masters to indicate their processing mode. A privileged processing mode typically has a greater level of access within a system.
Secure or non-secure
This is used in systems where a greater degree of differentiation between processing modes is required.
Instruction or data
This bit gives an indication if the transaction is an instruction or a data access.
REGION identifiers means a single physical interface on a slave can provide multiple logical interfaces, each with a different location in the system address map. The use of the region identifier means that the slave does not have to support the address decode between the different logical interfaces.
USER defined signal. Must be supported by all interacting peripherals in the system

## Slide 10: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
Custom IP
Summary

## Slide 11: AXI4-Lite Slave
AXI4-Lite is a subset of AXI (Full)
  Same channels, but less signals than full interface
5 AXI channels
  Inputs: Write Address, Data; Read Address
  Outputs: Write Response; Read Data
Slave responds to read and write transactions from upstream Master
1 data transfer per transaction
  No burst support
Intended for lower performance peripherals
AXI Interconnect
AXI4-Lite IP (Slave)
User IP
AXI Transaction logic
(Ready, Valid, Response)
Write Response
Read Addr
Read Data
Write Data
Write Addr
Registers
led_ip_v1_0_S_AXI.v
led_ip_v1_0.v
lab3_user_logic.v

## Slide 12: AXI Lite Slave Single Data Phase Write
input
output
Notes: The write and read transactions are initiated by the upstream or Master device. The slave responds to the transaction request

## Slide 13: AXI Lite Slave Single Data Phase Read
input
output

## Slide 14: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
Custom IP
Summary

## Slide 15: AXI4-Lite Master
5 AXI channels
  Outputs: Write Address, Data; Read Address
  Inputs: Write Response; Read Data
Opposite directions to Slave
Master can initiate read and write transactions
1 data transfer per transaction
  No burst support
Addressable register bank in slave
Write Response
Read Addr
Read Data
Write Data
Write Addr
AXI Interconnect
AXI4-Lite IP (Master)
User IP
AXI Transaction logic
(Generate transactions, Ready, Valid)
<ip_name>_v<1_0>_S_AXI.v
<ip_name>_v<1_0>.v
<filename>.v

## Slide 16: AXI4-Lite Master Single Data Phase Write
input
output
Notes: Read and write transactions are initiated by the Master. Signals are similar to AXI4-Lite Slave, but channels are in the opposite direction.

## Slide 17: AXI4-Lite Master Single Data Phase Read
input
output

## Slide 18: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
Custom IP
Summary

## Slide 19: AXI4
Superset of AXI4-Lite
Extra signals to support additional features
  Burst transactions
  Transaction ordering
Not all AXI4 signals used by Xilinx IP
  Ignored, or Pass through
Single Read/Write transactions similar to AXI lite
  Transaction ID
  LAST signal
Memory space
AXI4 IP (Slave)
User IP
AXI Transaction logic
(Ready, Valid, Response)
Address space
my_slave_ip_v1_0_M_AXI.v
my_slave_ip_v1_0.v
user_logic.v

## Slide 20: AXI4
Superset of AXI4-Lite
Extra signals to support additional features
  Burst transactions
  Transaction ordering
Not all AXI4 signals used by Xilinx IP
  Ignored, or Pass through
Single Read/Write transactions similar to AXI lite
  Transaction ID
  LAST signal
Example of read from AXI4 BRAM

## Slide 21: AXI4 Read Transaction Multiple reads, not burst transaction
Multiple read transactions are identified by different read IDs
  For a burst transaction only one read ID would have been used
Separate RLAST for corresponding read transactions
ARSIZE=2 indicates 4 bytes are being read
  0 : 1 byte
  1 : 2 bytes
  2 : 4 bytes
Example of multiple reads from AXI4 BRAM

## Slide 22: AXI4 Write Transaction
Example of AXI4 write transaction

## Slide 23: AXI4 Write Transaction Multiple write, not burst
Multiple write transactions are identified by different write IDs (AWID)
  For a burst transaction only one write ID would have been used
Separate OKAY status for corresponding write transactions
WSTRB=0xF indicates entire word is being written
Example of AXI4 multiple write transactions

## Slide 24: AXI4 Write Burst Burst Data Phase 4 Writes
Single Burst transaction
  AWLEN = 3 (Burst Size)
  Length = AWLEN+1 (4 transactions)
INCR from Base AWADDR
WSTRB=0xF indicates entire word is being written
LAST indicates end of burst
  AWLEN also indicates the size of the burst
A burst must not cross a 4KB Boundary
Example of AXI4 write burst transaction
Notes: The AXI burst Slave Attachment block supports fixed bursts of bytes, half-words, words, double-words, and quad words with transfer lengths of:
1 to 256 data beats with INC type transfers
1 to 16 data beats with FIXED type transfers
2, 4, 8, 16 data beats with WRAP type transfers
The figure above shows a burst request from a 32-bit master to the 32-bit slave.

## Slide 25: Documentation
Xilinx AXI Reference Guide, UG761
  AXI Usage in Xilinx FPGAs
    Introduce key concepts of the AXI protocol
    Explains what features of AXI Xilinx has adopted
ARM specifications
  AMBA AXI Protocol Version 2.0
  AMBA 4 AXI4-Stream Protocol Version 1.0
  http://infocenter.arm.com/help/topic/com.arm.doc.set.amba

## Slide 26: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
  Package IP
  Create IP
Summary

## Slide 27: Reusing Your IP
IP from many sources can be packaged and made available in Vivado
All IP available in the Vivado IP Catalog can be used to create IP Integrator designs
Any IP Integrator diagram can be quickly packaged as a single complex IP
IP Packager
Source (C, RTL, IP, etc)
Simulation Models
Documentation
Example Designs
Test Bench
Vivado IP Integrator
Standardized IP-XACT representation
IP Catalog
Xilinx IP
3rd Party IP
User IP
Notes: Vivado supports reuse of IP is by providing users a means to capture their individual IP or IP subsystems and package that IP, and then make the IP available to other users through the Vivado IP catalog. This approach also benefits third party IP providers, who now have a standard way of providing their IP for both evaluation and purchase, and that IP will be visible through the IP Catalog.
Packaging an IP Integrator diagram takes one Tcl command, or several mouse clicks.

## Slide 28: Create and Package IP
The Create and Package IP wizard allows you to
  Create a template for a new peripheral
  Package the current project
    Only available if project is open
  Package an existing project
The packager allows IP to be included in the IP Catalog for distribution
It uses IP-XACT format
Complete set of files included
  Source code, Constraints, Test Benches (simulation files), documentation

## Slide 29: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
  Create IP
  Package IP
Summary

## Slide 30: Create Custom IP
Create and Package IP Wizard
Generates HDL template for
  Slave/Master
    AXI Lite/Full/Stream
Optionally Generates
  Software Driver
    Only for AXI Lite and Full slave interface
  Test Software Application
  AXI4 BFM Example

## Slide 31: Create Custom IP
Add IP to repository
Edit IP
Verify
  BFM Simulation Example Design
  JTAG

## Slide 32: Generated Template for AXI Lite
HDL implementation of AXI Interface
  32 bit data width
User specifies required number of registers (minimum 4)
Read/write to/from Registers implemented
User logic can be easily connected
User logic can be a hierarchical design

## Slide 33: HDL AXI Lite
Connect user logic to registers, or modify design
Address
Register
Data

## Slide 34: Generated Template for AXI Full
HDL AXI Full Interface
  32 bit data interface
Burst transaction support implemented
  Specify size of memory space
  Up to 1024 Bytes
Example code implementing block memory
  User logic can connect or replace this section

## Slide 35: Files created
component.xml
  IP XACT description
bd
  Block Diagram tcl file
drivers
  SDK and software files (c code)
  Simple register/memory read/write functionality
  Simple SelfTest() code
hdl
  Verilog/VHDL (should be inside project directory
xgui
  GUI tcl file

## Slide 36: Edit IP
New Vivado project will open
Template files have been generated and are added to the project
IP can now be edited
  Modify existing template files, add user source files
IP Packager will be open
  Last step is to Package IP

## Slide 37: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
  Create IP
  Package IP
Summary

## Slide 38: Package IP
Package current project
  Must be open!
  Package generated HDL
Package a directory (another project/source files)
  Option to package as a library core
  Core can be referenced by other IP
  Core not available standalone (Will not display in IP Catalog)
Create New AXI4 Peripheral (previous section)
  Will also need to be packaged
  Similar steps to package for all three flows

## Slide 39: IP-XACT
Industry Standard (IEEE) XML format to describe IP using meta-data
  Ports
  Interfaces
  Configurable Parameters
  Files, documentation
IP-XACT only describes high level information about IP, not low level description, so does not replace HDL or Software.
Enables automatic connection, configuration and integration
Enables integration of 3rd Party IP
  (And Export of your own IP)

## Slide 40
IP Packager
Automatically analyze project/files to determine parameters
Initial Summary
Identifies
  Files
    Source HDL, Testbenches, Documentation,
  Parameters
    Configurable
  Ports
  Interfaces
  Compatibility
Creates GUI Layout for IPI

## Slide 41: IP Packager
Modify configuration
  Properties
  Compatibility
  Files
  Custom parameters
  Ports
  Interfaces
  Address and Memory
  IP and security
Project can be updated – e.g. source files added
  Changes will be reflected in packager
Review and package

## Slide 42: Customizing IP for Reuse in IP Packager
Add, Edit or change defaults
Select
Options
Notes: The packager handles all the IP-XACT specific file creation, manages IP versions, recognizes interfaces, and creates customized configuration dialogs, as well as more advanced functionality.

## Slide 43: IP repository
The Vivado IP Catalog can be extended by adding additional IP Repositories.
Third party IP, your custom IP, and Xilinx IP are displayed in an identical manner
Packager creates .xml file for the IP
Specify the directory of the user/third party IP repository
  Can be done automatically from packager
  Access from project settings, or IP Catalog
  Displays the IP that has been found
Displays IP in the repository for use in IPI

## Slide 44: Creating and Using custom IP summary
Create and modify Template (add user logic) or create IP manually
Package IP
  Specify configuration settings
Specify IP directory in the Vivado repository
  Project settings
Available to use in IP Catalog like any other IP

## Slide 45: Outline
AXI4 Transactions
  AXI4-Lite Slave
  AXI4-Lite Master
  AXI4 Slave/Master
Create and Package IP
Custom IP
Summary

## Slide 46: Summary
AXI4 interface defines five channels
  All channels use basic VALID/READY handshake to complete a transfer
AXI Interconnect extends AXI interface by allowing 1-to-N, N-to-1, N-to-M, and M-to-N connections
Custom IP can be imported using IP Packager
Include in the IP Repository for reuse across projects
Create and Package wizard supports AXI Lite, Full, and Stream compatible IP creation and packaging
  Handles interface side protocol
  Provides template to add HDL functionality
  Packages into the IP Catalog