## Slide 1: Software Development Environment
Zynq
Vivado 2014.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Understand the basic concepts of the Eclipse IDE in SDK
  List SDK features
  Identify the GNU tools functionality
  List steps in creating a software application
  State when address management is needed
  Describe the object file sections
  Describe what a linker script does

## Slide 3: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 4: Desktop versus Embedded
Desktop development: written, debugged, and run on the same machine
OS loads the program into the memory when the program has been requested to run
Address resolution takes place at the time of loading by a program called the loader
  The loader is included in the OS
The programmer glues into one executable file called ELF
  Boot code, application code, RTOS, and ISRs
  Address resolution takes place during the gluing stage
The executable file is downloaded into the target system through different methods
  Ethernet, serial, JTAG, BDM, ROM programmer

## Slide 5: Embedded versus Desktop
Development takes place on one machine (host) and is downloaded to the embedded system (target)
Host Computer
Target Board
A cross-compiler is run on the host
JTAG
UART

## Slide 6: Embedded Development
Different set of problems
  Unique hardware for every design
  Reliability
  Real-time response requirement (sometimes)
    RTOS versus OS
  Code compactness
  High-level languages and assembly
Notes: Every embedded system design is unique in its function and targeted for a unique application. A design developed for one application may not work for another embedded system. Another issue is reliability. Because the system is standalone, and a combination of hardware and software, the design may have some hidden bugs that can make the system malfunction. Therefore, such a system may not be one hundred percent reliable. Depending on the application, the system may require real-time response and RTOS use, which can lead to bigger code and a larger memory requirement. Real-time systems also require assembly language programming for time-critical applications.

## Slide 7: Software Development Tools

## Slide 8: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 9: SDK Application Development Flow

## Slide 10: Eclipse/CDT Frameworks of SDK
Builder framework
  Compiles and Links Source files
  Default Build options are specified when application is created: Choice of Debug, Release, Profile configurations
  User can custom build options later when developing application
  Build types: Standard Make, Managed Make
Launch framework
  Specifies what action needs to be taken: Run (+ Profile) application or Debug application
  In SDK, this is akin to the Target Connection settings
Debug framework
  Launches debugger(gdb), loads application and begins debug session
  Debug views show information about state of debug session
Search framework
  Helps development of application
Help System
  Online help system; context-sensitive

## Slide 11: Workspaces and Perspectives
Workspace
  Location to store preferences & internal info about projects
  Transparent to users
  Source files not stored under Workspace
Views, Editors
  Basic user interface element
Perspectives
  Collection of functionally related views
  Layout of views in a perspective can be customized according to user preference
Notes: The SDK "Workspace" is a cumulative catalog of all application projects you create using SDK, independent of the target design. The workspace allows you to navigate between application projects to ease code reuse without having to locate the project directories in the file system. The workspace also acts as a registry to remember all your project settings. SDK creates the workspace in a predefined location when you first invoke the tool.
A perspective is a layout of views (development tools) in the Workbench window. Each type of perspective is a combination of views, menus, and toolbars that enable you to perform a particular task. For example, the C/C++ perspective has views that are organized to help you develop C/C++ programs; the Debug perspective has views that enable you to debug those programs.

## Slide 12: Views
Eclipse Platform views: Navigator view, Tasks view, Problems view
Debug views: Stack view, Variables view
C/C++ views: Projects view, Outline view

## Slide 13: C/C++ Project View
Hierarchical list of the workspace projects in a hierarchical format
Double-click to open a file
Right-click the project to access its properties
Software Applications
Hardware Description
Software BSP
Software Applications
Notes: There are three kinds of projects: hardware platform, software Board Support Package (BSP), and software application projects.
There must be at least one hardware platform project workspace.
There must be at least one software board support package project per hardware processor instance.
There can be many software application projects, each one being associated with a BSP project.

## Slide 14: Outline View
Displays an outline of the structured file that is currently open in the editor
The contents of the outline view are editor specific
Content type is indicated by the icon
For a C source, icons represent
  #define statements
  Include files
  Function calls
  Declarations
Selecting a symbol will navigate to the same in the editor window

## Slide 15: C/C++ Perspective
C/C++ project outline displays the elements of a project with file decorators (icons) for easy identification
C/C++ editor for integrated software creation
Code outline displays elements of the software file under development with file decorators (icons) for easy identification
Problems, Console, Properties view lists output information associated with the software development flow
Project Outline
Editor View
Code Outline
Console

## Slide 16: Opening Perspectives and Views
To open a Perspective, use
  Window  Open Perspective
To open a view, use
  Window  Show View
  If the view is already present in the current perspective, the view is highlighted

## Slide 17: Editor
Syntax Highlighting
  bracket matching
  syntax coloring
  content assist
  refactoring
  keyboard shortcuts

## Slide 18: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 19: Launching SDK
Launch SDK
  Standalone
    Choose workspace, choose Hardware Platform Specification
  In Vivado
    File> Export
    File > Launch SDK
  Block Diagram needs to be Open before exporting
    A Hardware Description File HDF file is first generated
    A hardware platform specification project is then automatically created
      The software application (and board support package) then can be created and associated with the hardware platform

## Slide 20: Creating a Board Support Package
  The Board Support Package provides software services based on the processor and peripherals that make up the processor system
  Can be automatically created when creating Application project
Can be created standalone
Must be attached to a Hardware Platform
  In SDK, File > New > Xilinx Board Support Package
  Select appropriate OS support
  Third-party operating systems are supported with the appropriate BSP selection
  Select required libraries support

## Slide 21: Creating a Software Application Project
SDK supports multiple software application projects
A software project is attached to a BSP project
Sample applications are provided
  Great for quick test of hardware
    Peripheral Tests
  Starting point to base your own application on
Typically an Empty Application is opened to begin a non-standard project

## Slide 22: Directory Structure
SDK projects are place in the application directory that was specified when SDK was launched
Each project may have multiple directories for system files and configurations
Configurations are property tool option permutations of the software application. Each configuration has project properties set depending on needs. An ELF file is generated for each
  Release configuration
  Debug configuration
  Profile configuration
A Debug configuration is created by default
Notes: Configurations are used to maintain different tool options for software in different states of design, profile, debug, and release.
SDK has another selection of RUN configurations, described later.
Do not confuse the fact that the SDK tool defines configurations in two distinct tool areas.

## Slide 23: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 24
Simulation
Generator
Hardware
Platform Generation
Library Generation
Embedded Software
Development
IP Library or User Repository
MSS
Library Generation
.a
Compiler (GCC)
.o, .a
Linker (GCC)
ELF
IPI
Platform Generation
Drivers
.hdf
HDL
System and Wrapper HDL
system.bmm
Synthesis
Implementation
XDC
Bitstream Generation
system_bd.bmm
Configure BRAM
download.bit
Hardware Manager
system.bit
Simulation model
Generation
Behavioral VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation
IP Models
HDL Models
CompXLib
Application Source .c, .h, .s
Embedded Tool Flow (SDK)
SW Libraries
Libraries,
OS, MLD
XMD, TCF GDB
FPGA
JTAG Cable
Linker Script
SDK

## Slide 25: GNU Tools: GCC
GCC translates C source code into assembly language
GCC also functions as the user interface to the GNU assembler and to the GNU linker, calling the assembler and the linker with the appropriate parameters
Supported cross-compilers:
  GNU GCC (arm-xilinx-eabi-gcc)
Command line only; uses the settings set through the GUI

## Slide 26: GNU Tools: GCC
Calls four different executables
  Preprocessor (cpp0)
    Replaces all macros with definitions defined in the source and header files
  Language specific c-compiler
    cc1 C-programming language
    cc1plus C++ language
  Assembler
    arm-xilinx-eabi-as
  Linker
    arm-xilinx-eabi-ld
arm-xilinx-eabi-as
arm-xilinx-eabi-ld

## Slide 27: GNU Tools: AS
Input: Assembly language files
  File extension: .s
Output: Object code
  File extension: .o
  Contains
    Assembled piece of code
    Constant data
    External references
    Debugging information
Typically, the compiler automatically calls the assembler
Use the -Wa switch if the source files are assembly only and want to use the gcc

## Slide 28: GNU Tools: LD
Linker
Inputs:
  Several object files
  Archived object files (library)
  Linker script (mapfile)
Output:
  Executable image (.ELF)
  Map file

## Slide 29: GNU Utilities
AR Archiver
  Create, modify, and extract from libraries
  Used in SDK to combine the object files of the Board Support Package (BSP) in a library
  Used in SDK to extract object files from different libraries
Object Dump
  Display information from object files and executables
    Header information, memory map
    Data
    Disassemble code
Notes: The mb-objdump (powerpc-eabi-objdump) utility lets you see the contents of an object (.o) or executable (.out) file.
To see your symbol table, the size of your file, and the names or sizes of the sections in the file, run:
mb-objdump -x a.out
To see a listing of the (assembly) code in your object or executable file, run:
mb-objdump -d a.out
To get a list of other options, run:
mb-objdump --help

## Slide 30: Object Dump Display summary information from the section headers
Section
Name
Loadable Memory Address
Virtual Memory Address
Section Size
Byte alignment
Offset from the beginning of the section header table
arm-xilinx-eabi-objdump –h executable.elf

## Slide 31: Object Dump Dumping the source and assembly code
Memory location
C code instruction
Assembly instruction
Machine Language Instruction
arm-xilinx-eabi-objdump –S executable.elf

## Slide 32: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 33: Minimal Required Services
C language standard services
  C language construct services
  stdin and stdout
  Math library
  malloc
Processor support requires these services
  Interrupt
  Cache
  Language environment support

## Slide 34: Operating Systems
Operating systems are a collection of software routines that comprise a unified and standard set of system services
The Standalone option is used when no operating system is desired
  Provides a minimal amount of processor and library services as previously illustrated
  Can be considered a minimal, non-standard operating system
  Installed as a software platform
Variety of third-party operating systems are available
  Linux – many flavors
  RTOS – real-time operating system; also has many flavors; Free RTOS (an option for the Cortex™-A9 processor)
  XilKernel – provided by Xilinx; small and simple; only for MicroBlaze
Operating systems are installed and become part of the Board Support Package (BSP)

## Slide 35: What an Operating System Provides?
Operating system services
  GUI support
  TCP/IP services**
  Task management
  Resource management**
  Familiar programming services and tasks
  Easy connection to already written applications
  Ability to reload and change applications
  Full file system services**
  ** Also available as additions to the Standalone BSP

## Slide 36: Do I Need an Operating System?
The Standalone BSP includes the previously discussed items
Design considerations for systems using the Standalone BSP
  All services needed are included in the BSP
  The application is static—it never changes
  The application fits in block RAM (MicroBlaze™ processor), OCM RAM (Zynq™ AP SoC), or DDR memory
  The application is single-task based
  Interrupts may or may not be used

## Slide 37: Accessing Software Platform Properties
Select the created board support package in the Project Explorer view
Xilinx Tools > Board Support Package Settings
Sets all of the software BSP related options in the design
Has multiple forms selection
  Overview
  Standalone
  Drivers
  CPU
As individual Standalone services are selected a configurable menu selection item will appear
Notes: Open the Software Platform Settings dialog box by selecting Tools  Software Platform Settings. This dialog box has multiple forms and is used to set all the software platform-related options in the design.
Overview:
This form allows you to select the OS version and services.
You can also select available libraries support in this form. Depending on the library that you select in this form, a configuration panel menu selection will appear under the Standalone menu.
Standalone:
This form shows a list of all configurable devices (stdin/stdout). You can also select if you want to perform profiling and a timer to be used in profiling. If any library support is selected in the Overview form, and menu of the service’s configurable parameters will be presented under the Standalone menu.
Drivers:
This form allows you to specify values for the parameters associated with the peripheral drivers in the design.
CPU:
Tool chain options and their settings.

## Slide 38
Hardware
Platform Generation
Simulation
Generator
Library Generation
Embedded Software
Development
IP Library or User Repository
MSS
Library Generation
.a
Compiler (GCC)
.o, .a
Linker (GCC)
ELF
IPI
Platform Generation
Drivers
.hdf
HDL
System and Wrapper HDL
system.bmm
Synthesis
Implementation
XDC
Bitstream Generation
system_bd.bmm
Configure BRAM
download.bit
Hardware Manager
system.bit
Simulation model
Generation
Behavioral VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation model
Generation
Structural/Timing VHD Model
Simulation
IP Models
HDL Models
CompXLib
Application Source .c, .h, .s
Embedded Tool Flow (SDK)
SW Libraries
Libraries,
OS, MLD
XMD, TCF GDB
FPGA
JTAG Cable
Linker Script

## Slide 39: Library Generation Flow (in SDK)
Library Generator
Input files → MSS
  Output files → libc.a, libXil.a, libm.a
  LibGen is generally the first tool run to configure libraries and device drivers
    The MSS file defines the drivers associated with peripherals, standard input/output devices, and other related software features
  LibGen configures libraries and drivers with this information and produces an archive of object files:
    libc.a - Standard C library
    libXil.a - Xilinx library
    libm.a - Math functions library
Notes: Software Files
MSS
  An MSS file is supplied by the user as an input to the Library Generator (LibGen). The MSS file contains directives for customizing operating systems, libraries, and drivers
Linker script
  The linker script describes the mapping among all the sections in all the input object files and the output executable file. This file is used by the GNU linker
  Base System Builder will create a linker script for you
  If your address map specifies that the LMB, OPB, and external memory occupy contiguous areas of memory, you can use the BSB-created linker script to generate your executable
C/C++ source files
  Source code and header files written by the user

## Slide 40: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 41: C/C++ Build Settings
Right-click the top level of an application project and select C/C++ Build Settings
Most-accessed properties are in the C/C++ Build panel Settings tab
Each configuration has its own properties
Set options for this configuration
Tool settings for assembler, compiler, and linker

## Slide 42: Debug/Optimization Properties
Compiler optimization level
  None
  Low
  Medium
  High
  Size Optimized
Enable debug symbols in executable
  Necessary for debugging
  Set optimization level to none if possible

## Slide 43: Miscellaneous Compiler Properties
Define symbols for conditional compiling
  Add
  Delete
  Edit
References C source #ifdef symbol conditional statements #endif
Passed to compiler as –D option
Other compiler options are available
Add, Delete, Edit Icons

## Slide 44: Linker Properties
The Root panel displays properties for the selected configuration
Shown are the linker options for the Debug configuration
Default settings are fine for simple applications
Notes: The Linker Properties view allows you to set location of additional libraries (seldom used featrue. A typical example would be using the TCP/IP stack service contained in the Lwip library, an optional part of the Standalone BSP. The library requires the (-l) flag to be set to -llwip4.
The Miscellaneous tab allows other linker options to be set. Normally this is left blank. A possible use is to view the map cross-reference file that is not automatically generated by the linker. Use the following linker option to generate it: -Wl,-Map,outputfile.txt (no spaces).

## Slide 45: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 46: Address Management
Embedded processor design requires you to manage the following:
  Address map for the peripherals
  Location of the application code in the memory space
    Block RAM
    External memory (Flash, DDR3, SRAM)
Memory requirements for your programs are based on the following:
  The amount of memory required for storing the instructions
  The amount of memory required for storing the data associated with the program

## Slide 47: Standard ARM Programming Model
Processing system and programmable logic look the same
  AMBA® and AXI interfaces
  Memory-mapped I/O
  Register access
Consistency for PS and PL = ease of use
Memory map usage: total of 4 GB
  1 GB: DDR RAM
  2 GB: dedicated to PL peripherals
  1 GB: PS peripherals, OCM, external flash

## Slide 48: Programmer’s View of Programmable Logic
Programmable logic (PL) memory map
  2 GB total space
    1 GB for each AXI master: GP0, and GP1
  Accessible from any processing system (PS) master
    Either Cortex-A9 CPU
    PS DMA engine
    PS peripheral DMA engine
      Ethernet
      USB
      SD/SDIO
Custom Peripheral Code Snippet

## Slide 49: Address Map: I/O Peripherals (Zynq AP SoC)

## Slide 50: Address Map: SLCR Registers (Zynq AP SoC)

## Slide 51: Address Map: PS Registers (Zynq AP SoC)

## Slide 52: Address Map: CPU Private Bus Registers

## Slide 53: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 54: Object File Sections
What is an object file?
  An object file is an assembled piece of code
    Machine language: li r31,0 = 0x3BE0 0000
  Constant data
  There may be references to external objects that are defined elsewhere
  This file may contain debugging information

## Slide 55: Object File Sections Sectional layout of an object or an executable file
.text
.rodata
.sdata2
.sbss2
.data
.sdata
.sbss
.bss
Text section
Read-only data section
Small read-only data section (less than eight bytes)
Small read-only uninitialized data section
Read-write data section
Small read-write data section
Small uninitialized data section
Uninitialized data section
Notes: The .text section contains executable code. This section has the x (executable), r (read-only) and i (initialized) flags.
The .rodata section contains read-only data of a size more than 8 bytes (default). The size of the data put into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses.
The .sdata2 section contains small read-only data (size less than 8 bytes). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed with reference to the read-only small data anchor. This ensures that all data in the .sdata2 section can be accessed using a single instruction (a preceding imm instruction will never be necessary). This section has the r (read-only) and the i (initialized) flags.
This .sbss2 section contains small, read-only un-initialized data of a size less than 8 bytes. You can change the size of the data going into this section with the -G option. This section has the r(read) flag and can be mapped to ROM.
The .data section contains read-write data of a size more than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses. This section has the w (read-write) and the i (initialized) flags.
The .sdata section contains small read-write data of a size less than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed with reference to the read-write small data anchor. This ensures that all data in the .sdata section uses a single instruction (a preceding imm instruction will never be necessary). This section has the w (read-write) and the i (initialized) flags.
The .sbss section contains small uninitialized data of a size less than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. This section has the w (read-write) flag.
The .bss section contains uninitialized data of a size more than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses. The stack and the heap are also allocated to this section. This section has the w (read-write) flag.

## Slide 56: Sections Example
int ram_data[10] = {0,1,2,3,4,5,6,7,8,9}; /* DATA */
const int rom_data[10] = {9,8,7,6,5,4,3,2,1}; /* RODATA */
int I; /* BSS */
main(){
...
I = I + 10; /* TEXT */
...
}

## Slide 57: Object File Sections Reserved sections that you typically would not modify
.init
.fini
.ctors
.dtors
.got
.got2
.eh_frame
Language initialization code
Language cleanup code
List of functions to be invoked at program startup
List of functions to be invoked at program end
Pointers to program data
Pointers to program data
Frame unwind information for exception handling
Notes: The .init section contains language initialization code. This section has the same flags as .text. This must be mapped to initialized ROM.
The .fini section contains language cleanup code. This section has the same flags as .text. This must be mapped to initialized ROM.
The .ctors section contains a list of functions that must be invoked at program startup. This section contains the same flags as .data and must be mapped to initialized RAM.
The .dtors section contains a list of functions that must be invoked at program end. This section contains the same flags as .data and must be mapped to initialized RAM.
The .got2/.got sections contain pointers to program data. This section contains the same flags as .data and must be mapped to initialized RAM.
The .eh_frame section contains frame unwind information for exception handling. This section contains the same flags as .rodata and can be mapped to initialized ROM

## Slide 58: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 59: Linker Script
Linker script controls the linking process
  Map the code and data to a specified memory space
  Set the entry point to the executable
  Reserve space for the stack
Required if the design contains a discontinuous memory space

## Slide 60: Linker and Locator Flows
.text1
.data1
.bss1
foo1.o
foo2.o
0xFFFF
0xF000
0xEFFF
0xEF00
0x0000
0x1FFF
0x2000
0xEEFF
Locate
Merged Output Sections
Unused
Executable Image
Code
uninitialized data
Initialized data
.text2
.data2
.bss2
Link
.text
.data
.bss

## Slide 61: Linker Script Generator GUI
Table-based GUI allows you to define the memory space for code and data sections
Launch from Xilinx Tools > Generate Linker Script, or from the C/C++ perspective, right-click on <project> > Generate Linker Script
The tool will create a new linker script (the old script is backed up)

## Slide 62: Outline
Introduction
SDK Development Environment
SDK Project Creation
GNU Development Tools: GCC, AS, LD, Binutils
Software Settings
  Software Platform Settings
  Compiler Settings
Address Management
Object File Sections
Linker Script
Summary

## Slide 63: Summary
Software development for an embedded system in FPGA imposes unique challenges due to unique hardware platform
SDK provides many rich perspectives which enable ease of accessing information through related views
GNU tools are used for compiling C/C++ source files, linking, creating executable output, and debugging
Software platform settings allow inclusion of software library support
Compiler settings provide switches including compiling, linking, debugging, and profiling

## Slide 64: Summary
Embedded processor design requires you to manage
  Peripheral address space
  Memory address space to store data and instructions
    Internal block memory
    External memory
Linker script is required when the software segments do not reside in a contiguous memory space