## Slide 1: Lab4 Intro Writing Basic Software Application
Zynq
Vivado 2014.2 Version

## Slide 2: Introduction
This lab guides you through the process of writing a basic software application. You will add AXI BRAM controller and a BRAM memory.
Then you will create a software project in SDK and develop a software that will monitor dip switches and write to the LED_IP device to which LEDs are connected.
You will also modify a linker script file and view its effect on the sections location.
Finally, you will download the bit file and verify the functionality

## Slide 3: ARM Cortex-A9 based Embedded System Design Lab4: Add BRAM and develop software
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
AXI-BRAM Controller
Memory
GPIO
UART
RS232
DIP Switches
AXI4
AXI4-Lite
AXI4-Lite
GPIO
LED_IP
Push-Buttons
AXI4-Lite
LED
BRAM
M_AXI_GP0
PS
PL

## Slide 4: Procedure
Open project in Vivado
Add an internal BRAM
Generate bitstream and invoke SDK
Create a software project
Analyze assembled object files
Verify the design in hardware

## Slide 5: Summary
Use SDK to define, develop, and integrate the software components of the embedded system.
You can define a device driver interface for each of the peripherals and the processor.
SDK imports an xml file and lets you update the settings so you can develop the software side of the processor system.
You can then develop and compile peripheral-specific functional software and generate the executable file from the compiled object codes and libraries. If needed, you can also use a linker script to target various segments in various memories.