## Slide 1: Introduction to Embedded System Design using Zynq
Zynq
Vivado 2014.2 Version

## Slide 2: Objectives
After completing this module, you will be able to:
  Define a Zynq All Programmable SoC (AP SoC) processor component
  Enumerate the key aspects of the Zynq AP SoC processing system
  Describe the embedded design flow
  Understand the function of the IP Integrator tool
  Indicate how the hardware design is linked to the software development environment

## Slide 3: Outline
Embedded Processor Component
Overview of Vivado for Embedded System Design
Embedded System Development Flow
Hardware Platform Creation
SDK Software Platform
Summary

## Slide 4: Embedded Design Architecture in Zynq
Embedded design with Zynq is based on:
  Processor and peripherals
    Dual ARM® Cortex™ -A9 processors of Zynq-7000 AP SoC
    AXI interconnect
    AXI component peripherals
    Reset, clocking, debug ports
  Software platform for processing system
    Bare Metal Applications or OS’s (e.g. Linux, FreeRTOS)
    C language support
    Processor services
    C drivers for hardware
  User application
    Interrupt service routines (optional)

## Slide 5: The PS and the PL
The Zynq-7000 AP SoC architecture consists of two major sections
  PS: Processing system
    Dual ARM Cortex-A9 processor based
    Multiple peripherals
    Hard silicon core
  PL: Programmable logic
    Uses the same 7 series programmable logic
      Artix™-based devices: Z-7010, Z-7015 and Z-7020 (high-range I/O banks only)
      Kintex™-based devices: Z-7030, Z-7045, and Z-7100 (mix of high-range and high-performance I/O banks)

## Slide 6: PS Components
The Zynq AP SoC processing system consists of the following blocks
  Application processing unit (APU)
  I/O peripherals (IOP)
    Multiplexed I/O (MIO), extended multiplexed I/O (EMIO)
  Memory interfaces
  PS interconnect
  DMA
  Timers
    Public and private
  General interrupt controller (GIC)
  On-chip memory (OCM): ROM and RAM
  Debug controller: CoreSight

## Slide 7: Zynq Architecture Built-in Peripherals
Two USB 2.0 OTG/Device/Host
Two Tri- Mode GigE (10/100/1000)
Two SD/SDIO interfaces
  Memory, I/O and combo cards
Two CAN 2.0Bs, SPIs , I2Cs, UARTs
Four GPIO 32bit Blocks
  54 available through MIO; other available through EMIO
Multiplexed Input/Output (MIO)
  Multiplexed pinout of peripherals and static memories
Extended MIO
  Maps PS peripheral ports to the PL

## Slide 8: Outline
Embedded Processor Component
Overview of Vivado for Embedded Design
Embedded System Development Flow
Hardware Platform Creation
SDK Software Platform
Summary

## Slide 9: Vivado
What are Vivado, IP Integrator and SDK?
  Vivado is the tool suite for Xilinx FPGA design and includes capability for embedded system design
    IP Integrator, is part of Vivado and allows system level design of the hardware part of an Embedded system
    Integrated into Vivado
    Vivado includes all the tools, IP, and documentation that are required for designing systems with the Zynq-7000 AP SoC hard core and/or Xilinx MicroBlaze soft core processor
    Vivado + IPI replaces ISE/EDK
  SDK is an Eclipse-based software design environment
    Enables the integration of hardware and software components
    Links from Vivado
Vivado is the overall project manager and is used for developing non-embedded hardware and instantiating embedded systems
  Vivado/IP Integrator flow is recommended for developing Zynq embedded systems using 2013.2 and later

## Slide 10: Vivado Components
Vivado/IP Integrator
  Design environment for configuration of PS, and hardware design for PL
  Hardware Platform (xml)
  Platform, software, and peripheral simulation
  Vivado logic analyzer integration
Software Development Kit (SDK)
  Project workspace
  Hardware platform definition
  Board Support Package (BSP)
  Software application
  Software debugging
Hardware Design
Software Design
HW/SW Simulation
HW/SW Debug

## Slide 11: Embedded System Tools: Hardware
Hardware and software development tools
  IP Integrator
  IP Packager
  Hardware netlist generation
  Simulation model generation
  Xilinx Microprocessor Debugger (XMD)
  Hardware debugging using Vivado analyzer

## Slide 12: Embedded System Tools: Software
Eclipse IDE-based Software Development Kit (SDK)
  Board support package creation
  GNU software development tools
  C/C++ compiler for the MicroBlaze and ARM Cortex-A9 processors (gcc)
  Debugger for the MicroBlaze and ARM Cortex-A9 processors (gdb)
  TCF framework – multicore debug
Board support packages (BSPs)
  Stand-alone BSP
    Free basic device drivers and utilities from Xilinx
    NOT an RTOS

## Slide 13: Vivado View
Customizable panels
A: Project Management
B: IP Integrator
C: FPGA Flow
D: Layout Selection
E: Project view/Preview Panel
F: Console, Messages, Logs
A
B
C
D
E
F

## Slide 14: Zynq Customization Processing System
Block Configuration
PS-PL Interface Configuration
MIO Configuration/Table View
Clock Configuration
DDR
SMC Timing Calculation
Interrupt Configuration

## Slide 15: MIO Configuration

## Slide 16: MIO Configuration…

## Slide 17: Project Files
Top level Directory
  .xpr Vivado Project File (xml file), log files, journal
.srcs
  Project source files, IP Integrator files
.data
  Vivado database, internal data
.runs
  Synthesis, Implementation runs
.sdk
  SDK Export directory, Hardware Platform (xml)
.cache
  Temporary Files

## Slide 18: Outline
Embedded Processor Component
Overview of Vivado
Embedded System Development Flow
Hardware Platform Creation
SDK Software Platform
Summary

## Slide 19: Embedded System Design Flow for Zynq-7000 AP SoC

## Slide 20: Embedded System Design using Vivado
Create a new Vivado project, or open an existing project
Invoke IP Integrator
Construct(modify) the hardware portion of the embedded design
Create (Update) top level HDL wrapper
[optional] Synthesize any non-embedded components and implement in Vivado
Export the hardware description, and launch SDK
Create a new software board support package and application projects in the SDK
Compile the software with the GNU cross-compiler in SDK
[optional] Download the programmable logic’s completed bitstream using iMPACT
[optional] Use SDK to download the program (the ELF file)

## Slide 21: Embedded System Design using Vivado
11. Program bitstream & .elf into Zynq
Vivado
Hardware Configuration
IP Integrator
SDK
2. Invoke IP Integrator to create Block Diagram
5. Generate Top-Level HDL
6. Add Constraints
7. Generate Bitstream => .bit
8. Export hardware to SDK
3. Configure PS settings
4. Add IP & configure
(close Block Diagram, return to Vivado)
9. Specify hardware description from Vivado
10. Add Software Project & Build => .elf
1. Launch Vivado
ZYBO

## Slide 22: Add IP Integrator Block Diagram
IP Integrator Block Diagram opens a blank canvas
IP can be added from the IP catalog
Drag and drop interface
Intelligent Design environment
  Design Assistance
  Connection automation
  Highlights valid connections
  Group, create hierarchal blocks
Can create and import custom IP using IP Packager

## Slide 23: Configuring Hardware in IP Integrator
Double click blocks to access configuration options
Drag pointer to make connections
  Highlights valid connections
Connection Automation
  Automatically connect recognised interfaces
Automatically Redraw system

## Slide 24: Exporting to SDK
Software development is performed with the Xilinx Software Development Kit tool (SDK)
  Hardware configuration in Vivado
An XML description of the hardware is exported to SDK
  The hardware platform is built on this description
  Only one hardware platform for each SDK project
  (Optionally export bitstream)
The SDK tool will then associate user software projects to hardware

## Slide 25: Software Development Flow
Create hardware platform project
  Automatically performed when SDK tool is launched from Vivado project
Create BSP
  System software, board support package
Create software application
Create linker script
Build project
  compile, assemble, link output file <app_project>.elf

## Slide 26: Configuring FPGA and Downloading Application
Download the bitstream
  Only if PL is used
  Input file <top_name>.bit
The Vivado Hardware Manager (or Xilinx iMPACT tool) download the bitstream to the target
The bitstream can be downloaded from either
  Vivado
  SDK
Requires that the download cable is connected

## Slide 27: Outline
Embedded Processor Component
Overview of Vivado
Embedded System Development Flow
Hardware Platform
SDK Software Platform
Summary

## Slide 28: Zynq Configuration GUI
Provides a graphical view of the PS to configure
  ARM cores
  I/O peripherals
  DDR controller
  Memory systems
I/O partitioning between dedicated PS pins and programmable logic I/O
Zynq-7000 AP SoC PS is configured via a set of memory-mapped configuration registers

## Slide 29: Clock configuration
Clock Configuration
  Input frequency can be set
    Processor, DDR
  All IOP clock frequencies can be set
  Clock to PL configuration
  Set Timers

## Slide 30: Project Settings
Accessed from flow navigator
Default settings are typically used
Set/change target device
  Architecture, Device size, Package, Speed grade
Simulation, Synthesis, Implementation, Bitstream options
IP repository directory
  Provide path to custom IP not present in the current project directory structure

## Slide 31: Outline
Embedded Processor Component
Overview of Vivado
Embedded System Development Flow
Hardware Platform Creation
SDK Software Platform
Summary

## Slide 32: Software Development Kit (SDK)
Full-featured software design environment
Separate tool from Vivado – can install standalone for SW teams
Based on popular Eclipse open-source IDE
Used for software applications only; hardware design and modifications are done in Vivado
Well-integrated environment for seamless debugging of embedded targets
Sophisticated software design environment with many options and features with support for
  Multiple processors
  Multiple software platforms
  Multiple software applications
Fully Featured C/C++ code editor and error navigator

## Slide 33: SDK Workbench Views
C/C++ project outline displays the elements of a project with file decorators (icons) for easy identification
C/C++ editor for integrated software creation
Code outline displays elements of the software file under development with file decorators (icons) for easy identification
Problems, Console, Properties views list output information associated with the software development flow

## Slide 34: Software Management Settings
Software is managed in three major areas
  Compiler/Linker Options
    Application program
  Software Platform Settings
    Board support package
  Linker Script Generation
    Assigning software to memory resources
Covered in more detail later

## Slide 35: Outline
Embedded Processor Component
Overview of Vivado
Embedded System Development Flow
Hardware Platform Creation
SDK Software Platform
Summary

## Slide 36: Summary
Vivado includes all the tools, documentation, and IP necessary for building embedded systems
IPI is a System Level design tool that increases productivity, allowing designs to be completed faster
The Software Development Kit (SDK) is a comprehensive software development environment for software applications
An embedded processing system component is built with IP provided in the IP Catalog. Designers can also add their own custom IP to this catalog
The PS Configuration wizard permits access to several configurable features of PS